## Slide 1: Current Configuration Concerns
RGA
AGB
PDU
A single driveline disconnect from the PDU results in loss of door control.
A door obstruction results in damage to driveline components by the PDU.
Fewest number of LRUs – possible loss of door control.
RGA
AGB

## Slide 2: Config w/ O-brake and T-brake w/ CTS
RGA
AGB
PDU
O-Brake
TL
O-brake prevents uncontrolled door, T-brake protects downstream LRUs, CTS protects TS1 and PDU.
Ringfeder--Compliant TS (CTS)
1.1 A single driveline disconnect from the PDU (TS1, AGB, TS2 fail open)
1.1.1 Air loads backdrive RGAs and accelerate the door motion.
1.1.2 Shaft line overspeed (1.5 operating RPM) activates O-brake to lock and hold door position.
1.1.3 O-brake remains locked until manually reset.
1.1.4 Door rigging required before return to service.
1.2 An inadvertent lock of the O-brake while driveline still connected to PDU
1.2.1 Driveline torque increases to T-brake lock-out setting (aero limit load +30%).
  1.2.2 T-brake locks to stall PDU.
  1.2.2.1 If dynamic torque exceeds 3480 in-lbs, Ringfeder activates to absorb KE.
  1.2.2.2 Door rigging not required before return to service.
2 A door obstruction locks the T-brake which might activate CTS to protect TS1 and PDU.

## Slide 3: Overspeed Brake Overview

## Slide 4: LRU and ATP Sub-Assemblies
Seal and fasteners for joining the two sub-assemblies
RGA and Brake assemblies could be ATP’d separately.

## Slide 5: Parts Affected
New fixed ring gear
New end cap
New transition housing
New governor spring
(800 rpm < brake engagement < 1200rpm)
New thru shaft
(modified for gov spring height change)
New coupling
New thru shaft

## Slide 6: Brake Functionality
Ball ramp activated brake pack:
Angled faces convert shaftline torque into axial brake clamping force
Lock-out / Trip
Mechanism:
Prevents the ball ramps from separating during free running operation
Mechanical overspeed governor:
Fly balls in radial straight walled gutters, insensitive to angular acceleration
Manual reset:
Resets the friction plates to their normally gapped free running condition and returns the trip mechanism to its lock-out position.
Reset operation is opposed by residual torque across the ball ramps.

## Slide 7: Legacy Brake Trip Indication
Free
Running
Overspeed
Engagement
Friction plates gapped (0.030) axially
Engagement sensor (normally open) gapped
Reset lever
rotates 4 degrees
Sensor
(contacts closed)
Rotation speed flings balls outward
Ramp causes governor sleeve to move aft
Trip sleeve moves aft
Lock balls move inward
Ball ramps separate and clamp the friction plates

## Slide 8: Working in Progress Mechanic Trip Flag
Cam action
Spring return:
flag resets when brake is reset
Lug
Cross pin
Fork
(reset lever)
Flag
Flag
Plunger
Reset lever
Latch
(spring loaded)
Latch type
Spring extend:
Requires two operations
1 to reset the brake and
1 to reset the trip indicator

## Slide 9: Torque Limiter Overview

## Slide 10: Torque Limiter X-Section

## Slide 11: Compliant Toque Shaft Overview

## Slide 12: CTS Schematic

## Slide 13: Alt Configuration w/ Overspeed Brake w/ Fuse
RGA
AGB
PDU
OBRK
1.1 A single driveline disconnect from the PDU (TS1, AGB, TS2 fail open)
1.1.1 Air loads backdrive RGAs and accelerate the door motion.
1.1.2 Shaft line overspeed (1.5 operating RPM) activates O-brake to lock and hold door position.
1.1.3 O-brake remains locked until manually reset.
1.1.4 Door rigging required before return to service.
1.2 An inadvertent lock of the O-brake while driveline still connected to PDU
  1.2.1 If dynamic torque exceeds capability of shaft coupling, fuse shears and driveline disconnects
  from PDU.
1.2.1.2 Door position remains in its locked position.
  1.2.1.3 Door rigging required before return to service.
2 A door obstruction might shear the fuse to protect TS1 and PDU.
O-brake prevents single point loss of door control – permits secondary LRU damage.
Shear Coupling

## Slide 14: Shear Element Overview

## Slide 15: Shear Element Configuration
Baseline is “necked cylinder”
  Single component
  Loaded in torsional shear
  Minimizes or eliminates other load types
Shear element

## Slide 16: Load & Efficiency Summary
Boeing 8090200352 SCD Loads at RGA Output about Driveline
  Peak operating load for performance requirement: 83,214 in-lbf Limit Load: 258,255 in-lbf about RGA driveline per door (includes 1.15 NDD factor) Ultimate Load: 336,854 in-lbf about RGA driveline per door
System Efficiencies
  Room Temperature
    RGA: 70%, AGB: 96% HPDU: 89.1% (max from 8 set of data)
  Cold Temperature
  RGA: 35% (-65°F) AGB: 93% (-40°F) HPDU: 53.8% (-40°F estimated)
HPDU Static Output Torque (total for both shafts)
  2(3000)[.52/(2π)](6.0714) = 3015 in-lbf (100% eff)
  3015(.891) = 2686 in-lbf max with room temp eff
HPDU Max Driving Torque at Cold Temp (per door)
  83,214/[(.93)(.35)] = 255,650 in-lbf at RGA output
  255,650/[(16/9)(131.82)] = 1,091 in-lbf at HPDU output
Back Driving Loads at HPDU Output
  Limit Load at Room Temp: 258,255/[(16/9)(131.82)] = 1,102 in-lbf 100% eff
  1102(.96)(.70) = 740 in-lbf min room temp torque

## Slide 17: Interface and Installation
Actuator and torque shaft are replaced by RGA/O-Brake and torque coupling
Torque Limiter is located between angle G/B and Torque Shaft
Existing HPDU to Angle G/B shaft is replaced by Compliant T/S or Fusible T/S
Notes: 17

## Slide 18: Reliability
MTBF Summary
  Allocations provided to Parker.
  Overspeed Brake failure rate derived from legacy A-Brake observed failure rate.
  Torque limiter failure rate derived by NPRD Piece Part analysis.
LRU | Failure Rate Allocation (fpmh) | Predicted Failure Rate (fpmh) | Predicted MTBF (hours)
Overspeed Brake | N/A | 11.2516 | 88,876
RGA | N/A | TBD | TBD
Compliant Torque Shaft | 15.9755 | TBD | TBD
Torque Limiter | N/A | 14.2288 | 70,280
Fusible Shaft | 10.9755 | TBD | TBD