## Slide 1: Boeing MMA WBDDS SPF Mitigation Design Improvements SRR July 16, 2010

## Slide 2: SRR
Purpose is to gain concurrence that:
  Baseline exists
  Requirements are understood
  Ready to proceed to PDR

## Slide 3: SPECIFICATION COMMENTS
Table 1-1: SCD COMPLIANCE MATRIX - SPECIFICATION – 8090200352 – Weapons Bay Door Drive System (WBDDS) Rev G Draft 100707 |  |  | 
Para. Number | Title | CWFS Accepts (See Comments) | Comments
3.2.1.11 | Overspeed Brake | Exception | For the O-Brake design to be used “as proposed”, the speed of the drive shafts might have to be 2.25 times the maximum normal operating speed. Need further details to better estimate the limit
3.2.1.12 | Fusible Torque Shaft | ✓ | Will define/develop achievable shear-out range

## Slide 4: WBDDS Driveline Component Locations
The WBBDS incorporates two Over-Speed Brakes in each LH and RH drive trains.
AGB
189050-2
(1)
RGA
189053-1
(8)
AGB
189050-1
(1)
TS
189052-2
(2)
TS
189052-3
(2)
TS
189052-X
(2)
TS
189052-5
(2)
TC
189051-1
(4)
RGA/O-Brake Assy
Xxxxxx-1
(2)
Over-Speed Brake
RGA/O-Brake Assy
Xxxxxx-1
(2)

## Slide 5: O-brake Interface Design
Right Hand LRU
Left Hand LRU
Same as RH except
O-brake rotated 180º
Over-Speed Brake does not require hydraulic or electric interfaces.
Female spline mates with existing torque coupling
RGA interfaces
same as current
Over-Speed Brake

## Slide 6: LRU Sub-Assemblies
Over-Speed Brake is integrated with an RGA as one LRU.
Seal and fasteners for joining the two sub-assemblies
RGA and Brake assemblies could be tested separately.
Modified existing RGA
Modified existing Over-Speed Brake
Integration of O-brake and RGA into one LRU avoided airframe modification
Over-Speed Brake

## Slide 7: O-brake Minimum Engagement Speed
Sensitivity study to be preformed during preliminary design phase to predict lockout speed range.
New governor spring
(800 rpm < brake engagement < 1200 rpm)
Every legacy brake tested to +/- 200 rpm engagement speed requirement.
A review of the tolerance stack-ups and the legacy assembly shimming procedures planned for preliminary design phase to determine a higher minimum brake engagement speed for this application.
Over-Speed Brake

## Slide 8: Design
Isometric view (length not to scale)
Fusible Torque Shaft

## Slide 9: Design
Nut anti-rotation
Nut
Keyed washer / lock washer
Retaining wire / spring ring
Fusible Torque Shaft
Shaft coupling

## Slide 10: Design
Fusible Torque Shaft
Proposed Torque Shaft
Existing Torque Shaft
All changes pictured here

## Slide 11: Design
Existing lengths of tubing used in other versions of 189052 (456793)
Magneformed joints using existing geometry and materials of joint at spring loaded end of shaft
O-rings seal both sides of joint (left seal becomes dynamic after failure)
Shear element transmits torque until failure
Two sub-assemblies joined together by ball bearing and retaining nut
After shear element fails, two halves rotate relative to each other (assuming friction in seal and bearing << failure torque)
Couplings nearly identical to existing coupling, including same spline
Fusible Torque Shaft
Shoulders to prevent migration of shear element

## Slide 12: Design
Torque Limiter - Optional
Existing AGB Interface
Existing Torque Shaft Interface

## Slide 13: Torque Limiter
Torque Limiter - Optional
Jam Spring
Jam
Carrier
Through-Bolts (3)
Output Shaft
Control Spring
Input Shaft

## Slide 14: Location
The Torque Limiter will have a male spline output that mates to the AGB. The TL mounting pad will bolt to an aircraft bracket mounted between stiffeners using eight ¼ inch diameter bolts (four per side). The FTS will couple to the input side of the TL with the same spline interface as the TL to AGB interface.
Torque Limiter - Optional
AGB
TL
FTS

## Slide 15
Design Verification TP
O-Brake development
  Validate overspeed mechanical trip response
Shear element development
  Component level testing
    Static tests
      Validate sizing
      Determine variability at room temperature
    Endurance/fatigue
  Assembly level testing
    Static tests
      Determine influence of assembly on failure torque
    Dynamic tests
      Endurance/fatigue test to determine influence of shaft operating dynamics on shear element
      Simulate brake trip to validate failure at correct level
Preliminary Development/Prototype Testing

## Slide 16: Actuator ATP
Actuator Run-in
Actuator Efficiency
Free Play
Limit Load
Free Running Torque

## Slide 17: O-Brake ATP
Free Rotation
Mechanical Overspeed Trip
Holding Torque
Reset Indication
Limit Strength
Mechanical Trip Response

## Slide 18: O-Brake Assembly ATP
Free Running Torque
Finish & Workmanship
Weight
Interface Dimensions
Nameplate marking

## Slide 19: Fusible Torque Shaft ATP
Proof Load
End Coupling Retention
Weight
Nameplate Marking
Interface Dimension
Finish & Workmanship
Cleanliness

## Slide 20: Torque Shaft ATP – Same as current TS
Limit Load
End Coupling Retention
Weight
Nameplate Marking
Interface Dimension
Finish & Workmanship
Cleanliness

## Slide 21: Qualification Test Plan
Qual Test
  FTS
    Endurance Cycling
    Fatigue Buffeting
    Shock/Vibe
    Shear-out
  O-Brake
    Endurance Cycling
    Fatigue Buffeting
    Shock/Vibe
    Limit Load
    Ultimate Load
Test Rigs
  FTS Qualification/Production Rig
  O-Brake Qualification/Production Rig

## Slide 22: Qualification Test Plan
Description | Boeing SCD Requirement | Verification Method |  |  |  |  | Verification Documentation
 | 8090200352 | Simil. | Insp. | Anal. | Demo. | Test | 
Fusible Torque shafts | 3.2.1.3 | X |  | X |  | X | Qualification by Test Unit A – Endurance/Fatigue Unit B – Shock/Vibe Unit C – Shear-out Unit D – Slave Unit E – Development
O-Brake sub-assemblies O-Brake assemblies | 3.2.1.10 | X |  | X |  | X | Qualification by Test Unit A – Endurance/Fatigue Unit E – Development Unit B – Shock/Vibe Unit C – Limit/Ultimate Unit D – Slave
Torque shafts | 3.2.1.3 | X |  |  |  |  | Qualification by similarity to qualified configuration, 189052-1 to -5
Verification Methods:
Inspection - is defined as visual examination, physical manipulation, weighing, and includes review of documentation controlling configuration.
Analysis – is defined as a technical evaluation of equations, graphs, and data.
Similarity – is defined as a qualitative comparison to a qualified product in a similar or more demanding application.
Test – is defined as the verification that a requirement is met by a thorough exercising of the hardware.
Demonstration – is defined as a simple un-instrumented test where success is determined by observation alone.
Qual Test Matrix

## Slide 23: O-Brake Qualification Plan
Test No. | Test Description | Acceptance Criteria (P/F = Pass/Fail) | Results | Boeing SCD 8090200352 Paragraph
1 | Endurance Test Unit A | Load: Endurance Profiles B, C, and D Cycles: 13,200 There shall be no visible damage & Pass functional ATP |  | 3.2..2.14.1
2 | Fatigue Test Unit A | With through shaft locked Load: 0 in-lbs to 215 in-lbs, then back to 0 in-lbs to the input shaft. Cycles: 43,200 There shall be no visible damage Pass functional ATP |  | 3.2..2.14.2 *3.2.5.1.3
6 | Limit Load Test Unit C | With through shaft locked Load: 2490 in-lbs to the input shaft. Hold for 30 seconds min. With O-Brake engaged Load: 2706 in-lbs to the input shaft. Hold for 30 seconds min. Verify limit load There shall be no visible damage & pass functional ATP |  | 3.2.2.12.2 *3.2.1.5
9 | Ultimate Load Test Unit C | With through shaft locked Load: 3740 in-lbs to the input shaft. Hold for 3 seconds min. With O-Brake engaged Load: 4068 in-lbs to the input shaft. Hold for 3 seconds min. There shall be no damage |  | 3.2.2.13 *3.2.1.1
* Parker 456791SCS

## Slide 24: FTS Qual Test Plan
Test No. | Test Description | Acceptance Criteria (P/F = Pass/Fail) | Results | Boeing SCD 8090200352 Paragraph
2 | Endurance Test Unit A | Load: Endurance Profiles B, C, and D Cycles: 13,200 There shall be no visible damage & Pass functional ATP |  | 3.2..2.14.1
3 | Fatigue Test Unit A | With one end of the FTS locked Load: 0 in-lbs to 564 in-lbs, then back to 0 in-lbs to the input Fwd driving load 890? shaft. Cycles: 43,200 There shall be no visible damage & Pass functional ATP |  | 3.2..2.14.2 *3.2.5.1.3
2/3 | Shock / Vibe Unit B | Vibe test per Figure 6 & Shock test per Figure 7 Performance test durations are on hour per axis, Endurance test durations: 10 hrs per axis – 1 hr per axis under load and the remaining exposure time unloaded. There shall be no visible damage & pass functional ATP | MPI & FPI for any indications of cracks. | 3.1.3.1 *3.2.5.1.3.7 *3.2.5.1.3.8
6 | Shear-out Load Unit C | With one end of the FTS locked Load: 1437 to 2003 in-lbs will be applied to the shaft. Held for 30 seconds min. The shear element shall shear |  | 3.2.2.12.2 *3.2.1.5

## Slide 25: Potential Mini QSR
The following Environmental Requirements can potentially be Qualified by Similarity to qualified baseline configuration of MMA WBDDS Program, per EPR 06-104.

## Slide 26: QSR
Item No. | Test | 8090200352 SCD para. # | Test Specification | EPR 06-104
1 | Humidity | 4.1.3.2 | DO-160E, Sect. 6 Category C | Ref. Para 3.2.1
2 | Waterproofness | 4.1.3.3 | DO-160E, Sect. l0 Category S | Ref. Para 3.2.2
3 | Fluid Susceptibility | 4.1.3.4 | DO-160E, Sect. l1 Category S Including BMS3-11 Hyd. Fluid | Ref. Para 3.2.3
4 | Temperature & Altitude | 4.1.3.5 | DO-160E, Sect. 4 Category D2 | Ref. Para 3.2.4
5 | Decompression | 4.1.3.6 | DO-160E, Sect. 4.6.2 | Ref. Para 3.2.5
6 | Overpressure | 4.1.3.7 | N/A | N/A
7 | Fungus | 4.1.3.8 | DO-160. Sect. 13.3 Category F | Ref. Para 3.2.6
8 | Salt Spray | 4.1.3.9 | DO-160E, Sect. 14.2 Category S | Ref. Para 3.2.7
9 | Explosion-Proof | 4.1.3.12 | N/A | N/A

## Slide 27: QSR
Item No. | Test | 8090200352 SCD para. # | Test Specification | EPR 06-104
10 | Icing | 4.1.3.17 | DO-160E, Sect. 24 Category B | Ref. Para 3.2.9
11 | Sand & Dust | 4.1.3.18 | DO-160E, Sect. 12 Category S | Ref. Para 3.2.10

## Slide 28: Exit Criteria
To Close The SRR Meeting
  Reach concurrence that baseline exists
  Reach concurrence that requirements are understood
  Gain concurrence that WBDDS SPF Mitigation Configuration is ready to proceed to PDR