## Slide 1
WBDDS Single Point Failure SRR
P8A Weapons Bay Door Drive System
7-14-10
Notes: 1

## Slide 2: Agenda
PMR Action Item Review Hofer
Single Point Failure SCD Review Cameron
Key WBDDS Single Point Failure Performance Parameters Edwards
CWC Flowdown Overview Edwards
Test / Qualification Plan Overview Johnson/Doan
Schedule Review Hofer/Johnson

## Slide 3: PMR Action Item Review
Scott Hofer

## Slide 4: Single Point Failure SCD Review
Dean Cameron

## Slide 5: Key WBDDS Single Point Failure Performance Parameters
David Edwards

## Slide 7: Overspeed Brake Key Parameters
Single limit air load requirement versus limit load requirement at the open and closed positions
Imin = 65.4 in-lbf-s2
Lmax = 505.9 in-lbf-s2
Iopen = 318.6 in-lbf-s2
Acceleration per unit load at the door open position is much less than the closed position due to 5 times more inertia at the open position
The limit air loads are less in the closed position, which needs to be taken advantage of to reduce peak door acceleration in the closed position

## Slide 8: Overspeed Brake Key Parameters
Assumptions and Observations from Initial Analysis Results
  Intermediate door positions that do not result in structure impact may have high transient speeds but are considered for peak transient loading
  Door may impact structure repeatedly below overspeed set point but will not extend beyond one flight
  Worst case condition for impact is a trip just before impact so that impact occurs at peak speed with limit air load applied to door
  100% backdriving efficiency in acceleration due to air loads
    Low efficiency may need to be measured to use reduced impact speeds into structure
Key System Requirements
Peak limit load (SCD 3.2.2.12.2): (258,255 in-lb NDD)/1.15 = 224,570 in-lb
Peak door closed limit load (max within 5 deg of structure): TBD
Peak door open limit load (max within 5 deg of structure): TBD
Results based on CWC measured value of 5.5 ms response time from trip point to initiation of deceleration. This is critical and needs a shall not exceed requirement.
Maximum normal operating speed: 800 rpm (7.04 RGA output rpm)
  Requires motor ATP revision to ensure max speed is not exceeded
Minimum Trip Point: 928(1.20) = 1,110 O-brake rpm (8.42 RGA output rpm)
Desired peak overspeed factor for 5 impacts: TBD
Max trip point overspeed factor for fatigue: 1.5X (1,110/800 = 1.4X currently)

## Slide 9: Overspeed Brake Key Parameters
Results with peak limit door air load requirement
  Door Closed Position
  Door closed inertia: (XXX RGA output) (XXX O-brake) in-lbf-s2
  Acceleration: (XXX rpm/s RGA output) (XXX O-brake rad/s2)
  Travel from set point to initiation of deceleration:
  Travel to come to rest: TBD
  Peak speed: (XXX RGA output) (XXX O-brake) rpm
  Peak overspeed factor:
  Door Open Position
  Door closed inertia: (XXX RGA output) (XXX O-brake) in-lbf-s2
  Acceleration: (XXX rpm/s RGA output) (XXX O-brake rad/s2)
  Travel from set point to initiation of deceleration:
  Travel to come to rest: TBD
  Peak speed: (XXX RGA output) (XXX O-brake) rpm
  Peak overspeed factor:

## Slide 10: Overspeed Brake Key Parameters
Limit Brake Transient Holding Load: XXX in-lbf (Based on ATP test data)
NDD Brake Holding Load: 1.15(XXX) = 3560 in-lbf (Current driveline requirement)
Ultimate Holding Load: 1.5(XXX) = 4640 in-lbf (Current driveline requirement)
Limit Through Shaft Load (Max FTS setting): XXX in-lbf
NDD Through Shaft Load: 1.15(XXX) = 3560 in-lbf (Current driveline requirement)
Ultimate Through Shaft Load: 1.5(XXX) = 4640 in-lbf (Current driveline requirement)

## Slide 11: Fusible Torque Shaft Sizing and Fatigue Analysis

## Slide 12: Fusible Torque Shaft Sizing and Fatigue Analysis
With plastic factor, size shear element for PH13-8Mo CRES, Cond H1000, B basis

## Slide 13: Fusible Torque Shaft Sizing and Fatigue Analysis
6 lives of fatigue cycling predicted with conservative 8th mean load and 15,000 cycles per life requirement from Endurance Test data

## Slide 14: CWC Flowdown Overview
David Edwards

## Slide 15: Overspeed Brake SCS Requirements
Parameter | Dimension | Value | Basis
Overspeed Brake |  |  | 
Max Transient Load at Lockup | in-lb | TBD | Initial base off of test data and follow up dynamic model of O-brake
Limit Load (Thru Shaft) | in-lb | 2,490 3,560 | Current OTS design Same as AGB & TS limit load
Limit Load (Holding Load) | In-lb | 3,560 | Current SCS (may increase due to transient load)
Ultimate Load (Thru Shaft) | in-lb | 3,740 4,640 | Current OTS design Same as AGB & TS ultimate load
Ultimate Load (Holding Load) | in-lb | 4,640 | Current SCS (may increase due to transient load)
 | in-lb |  | 
Comply with Boeing SCD revision G and upcoming Parker document 456791SCS

## Slide 16: Fusible Torque Shaft Load Summary
Parameter | Dimension | Value | Basis
Fusible Torque Shaft (FTS) |  |  | 
Peak dynamic loading | In-lbf | 1,080 | Conservative value from all endurance test load profiles
Min Torque (shear) Setting | in-lb | 1,437 | Allows application of door ultimate load without rupture
Max Torque Setting | in-lb | 2,000 | Design limit load of existing driveline hardware
Fatigue Life | in-lb | 850 | 8th mean loads based on endurance test data for door opening and closing for 15,000 cycles/life (includes endurance and door open fatigue test). Effects of maximum HPDU backlash have not been taken into account yet

## Slide 17: Test / Qualification Plan Overview
Neil Johnson / Ken Doan

## Slide 18: Schedule Review
Scott Hofer / Neil Johnson